## Slide 1: Powered by
Akis Kourtis - NCSR Demokritos
DPDK Enabled Virtual Traffic Classifier over SR-IOV accelerated networks

## Slide 2: vTC Progress
Successfully integrated vTC into DPDK framework
Performance Benchmark with 2 scenarios
  One physical DPDK vs PCAP
  One virtualized, on SR-IOV enabled environment
    DPDK vs PCAP
All scenarios are done with DPDK vs PF_RING vs Docker(PF_RING)
Implementation of a SR-IOV environment with near line-rate capabilities
DPDK integration on a virtualized environment
OpenStack traffic mirroring implementation, with OVS manual modifications.

## Slide 3: Standard Architecture

## Slide 4: SR-IOV Enabled Architecture with DPDK

## Slide 5: SR-IOV Enabled Architecture with DPDK

## Slide 6: Experimental results for all scenarios

## Slide 7: OpenStack Deployment
VNF deployments in an OpenStack generate various networking issues
  Service Function Chaining (SFC)
  Traffic forwarding / Mirroring
  Inter-VM communication
VNFC is directly connected to virtual network interface of another VNFC’s,
Requires modification of Neutron’s OVS.
Each virtual network interface of a VNFC is reflected upon
  one TAP-virtual network kernel device
  a virtual port on Neutron’s OVS
  a virtual bridge connecting them.

## Slide 8: OpenStack Deployment
Direct connect virtual kernel interfaces of the 2 VNFCs
  Tap interfaces need to be shut down
  Removed from the OVS-OpenStack br-int
  Kernel Bridges removed
  Openflow rule application at the Neutron OVS
  All-forwarding policy between VNFC1 -> VNFC2
  Tap interfaces up again in promiscuous mode!
All traffic goes from VNFC1 to VNFC2, no questions asked!